## Slide 1: Swinburne University of Technology MATLAB Programming- Lab Week # 2 Course: MEE20007 Associate Professor Dr Ambarish Kulkarni 9/03/2023
Topics Covered:
Programming in Matlab
Relational and Logical Operations
Matlab Program Control
If-then-else For loop
Switch – case structures
While-break statements

## Slide 2: The power of MATLAB lies in its programming capability. There is a huge number of built-in and unlimited user defined functions that can be used in a Matlab program to perform complex engineering tasks and solve tedious computational problems. Before describing the
programming options available and their appropriate syntax, it must be understood that all the programming constructs employ the notations of some relation among its variables for decision making. A relation has the general form in MATLAB as {matrix} {relation} {matrix}.
The relational operations are:
== equals
~= not equal
< less than
<= less than or equal
> greater than
>= greater than or equal
Another useful set of operators used in relational expressions are logical AND, OR and NOT. These
are generally applied on matrices obtained from a relational matrix.
&
|
~
means "and", means "or" means "not"

## Slide 3
The value returned by a relation is a matrix containing zeros and ones. An entry is 0 if the matrix entry relation is FALSE and 1 if it is TRUE.
For example, Create two matrices T1 and T2 as:
>> T1= [1 1;0 1]; T2=[1 0;0 0]. Then apply AND (&) operator on T1 and T2 like
>> T=T1&T2. The result will be a matrix T=[1 0; 0 0] Similarly, application of OR (|) operator like
>> T=T1|T2 returns the matrix T=[1 1;0 1]
Finally, the NOT operator simply changes 1 to 0 and 0 to 1 like
>> T=~T1 gives the matrix T=[0 0;1 0]
The outcome of EQUAL (==) operator provides a comparison on the basis of equality of
corresponding elements in the two matrices. For example, if
>>A=[1 2;3 4]; B=[1 2;2 4] then
>>T1= A == B will return the matrix T1 =
1 1
0 1 --- where '1' is True and '0' is False w.r.t. the tested relation.
Try these other examples T2= A <= B
T3= A > B T4= A <= 3 T5= A ~= B

## Slide 4: Matlab Program Control
Matlab is a powerful programming language
if – then - else statements
switch - case statements
for loops
while loops
break statements
If Statements are used for Decision making
For developing a program you need to carefully There are three ways to apply ‘if' types:
understand about the structures and commands (a) if that generate specific controls in a program.
test expression statements
built around the syntax of C++. The following end
programming structures are available in Matlab: Here is some code which demonstrates the use
of IF statements. Type on the Matlab prompt.
>> A=[2 3]; % A is a 2-column row vector
>> if (A(1,1)<A(1,2)) % checks that if first element of A is less than second element of vector 'A' or not
A=[A;2*pi pi/2] % will execute this part if above
condition is TRUE
end
Note that row vector ‘A’ converts into matrix A

## Slide 5
(b) The ' if ' statement can be used with 'else' option, to cater for the possibility that the tested condition is not TRUE.
The syntax will be like:
if expression
statements
else
statements
end
Define a matrix ‘A’ and a row vector ‘B’ as shown below:
>> A=[6 7;8 9]; B=[4 5]
Type all that is below. You can move to next line by pressing ENTER,but be careful not to press ENTER key twice.
>> if (sum(A(:,2))
> 10 ) % check if sum of elements in second column >10
% executes these 2 statements if test condition is TRUE
 | A(1,1) | = | A(1,1) + B(1,1) %(Line 1) | 
 | A(2,1) | = | pi*A(2,1) % (Line 2) | 
else |  |  | % Moves to the next two lines if test condition is FALSE | 
 | A(1,1) | = | A(1,1) + A(1,1); %(Line 3) | 
 | A(2,1) | = | 0.5 * pi %(Line 4) | 
end --- NOW PRESS ENTER KEY. After execution, you should see the following result: |  |  |  | 
A = |  | 10 | 7 | % result of Line 1 execution
 |  | 8 | 9 | 
A = | 10.0000 |  | 7.0000 | % result of Line 2 coding
25.1327
9.0000

## Slide 6
(c) The “if” statements can include further alternate choices, using the optional keywords 'elseif' in addition to 'else'. The syntax will look somewhat like as given below:
if expression_1 statements
elseif expression_2 statements
elseif expression_3
.......................
else
statements
end
Let's consider a simple example. Type this program as a script file in MATLAB, numerals 1,2.. shows the line numbers as displayed in the script file:
% generates single random number under 100
% checks for smaller number (less than 30)
% tests for medium numbers (between 30 and 80) through logical 'and'
% finally declares the number large if above two conditions fail
1.
2.
3.
4.
5.
6.
7.
8.
a = randi(100, 1); if a < 30 disp('small')
elseif (a > 30 && a < 80) disp('medium')
else
disp('large')
end
Since the command 'randi' generates random numbers, so every time you repeat this sequence, you should get a different answer.

## Slide 7: Switch-case Statements:
If you need to select from or check among different options or choices of a single variable or condition, then switch-case is the control you need. A switch block conditionally executes one set of statements from several choices. Each choice is covered by a case statement.
The syntax of a switch-case statement can be given as below:
switch
case
case
expression [ can be a scalar or a string ] test1
command set 1
test 2
command set 2
......................................
otherwise
command set last
end
If expression is scalar, then ‘case’ is executed if the scalar value matches the expression in the test. If expression is a string value, then case is executed after matching of the string expression with the case string.

## Slide 8: **Here is a set of Matlab code to illustrate the operation of switch-case programming sequence. Please type it as a Matlab script file (.m) with the name “Units”.
disp('This program will convert your given value into centimetres')
x=input('Type the value:');
units = input('Enter the units: inch, mm or metre:','s');
switch lower(units) % converts your typed input to lower-case letters case {'in','inch'}
y = 2.54*x; % converts to centimeters
disp ([num2str(x) ' in ' units ' converted to cm is :' num2str(y)]) case {'m','meter'}
disp
y = x*100; % converts to centimters
([num2str(x) ' in ' units ' converted to cm is :' num2str(y)])
case { 'millimeter','mm'}
y = x/10;
disp ([num2str(x) ' in
' units ' converted to cm is :' num2str(y)])
(['unknown units:' units])
otherwise
disp
y = nan;
end
** Try to include the 'feet' option in the above program. **

## Slide 9: For Loop:
The "FOR" loop repeats the
The general form of a "FOR" loop is:
statement, ...,
END
The loop is executed in 4 steps:
Step 1: The "for" loop evaluates the entire expression at the time when the flow of control is transferred to the "for" loop. Step 2: The variable named next
to FOR keyword will be assigned the
given first value of the expression if the
statements a specific number of times. expression is a scalar, a row vector, or
a column vector. Step 3: The whole
block of command will be executed that
for variable = expression or values exists within the loop. Step 4: When the
"end" statement of the “FOR" is reached normally or by way of a "continue" statement, then the loop
variable will be assigned the next value
of the pre-determined expression. The statements is the block will be executed again for the new value.
Some examples are provided next:

## Slide 10
Examples of FOR loop in MATLAB:
(A) Type the following code in a script file:
N = 3
for R = 1:N % R represents number of rows for C = 1:N % C refers to number of columns
A(R,C) = 1/(R+C-1); % Generating rows and columns of
% matrix A.
end % Inner loop ends
end % Outer loop ends
Executing the loop will give you matrix A as follows:
A = | 1.0000 | 0.5000 | 0.3333
 | 0.5000 | 0.3333 | 0.2500
 | 0.3333 | 0.2500 | 0.2000
Your tasks:
1. Find out how Rows (R) and columns (C) of matrix 'A' are generated
2. How inner loop is executed within outer loop. Try to make a flow chart.
(B) The expression in "for" loop can have Step increments or decrements to give more control over the use of variable defined in the expression. For example type these lines in Command Window:
>> for s=1.0:-0.25:0 % a negative step with decrement of 0.25 with
% every repetition
a= s^2 end
Upon execution of these lines, few values will be displayed. Find out:
How many values were printed
What is the difference between successive values & why?

## Slide 11: While Loop – condition-based looping
The general form of the while loops are
while condition/expression
commands
end
Examples: (A) In the example below, the statements within "while – end" loop will be executed without break as long as the value of variable 'count‘ is less than 10.
count = 1; num = 2; % initializing the variables
while count < 10 % The commands within the loop will keep on executing till the test condition is FALSE
cnum= [count num]; % creates a vector disp(cnum) % displays the vector on screen num = num*2;
count = count + 1; % increase the value of count by 1.
end
Q. What is the meaning of the statement: count= count+1
What will happen in the absence of this statement.
(B) Another example is using while loop in finding out value of quadratic function. Make it a script file and save as QuadVal.m
% Script to compute value of “ax^2 +bx + c”
disp(’Quadratic ax^2+bx+c evaluated’)
disp(’for user input a, b, c, and x’)
a=1; b=1; c=1; x=0; % Initializing the values
while a~=0 | b~=0 | c~=0 | x~=0 disp(’Enter a=b=c=x=0 to terminate’) a = input(’Enter value of a: ’);
b = input(’Enter value of b: ’); c = input(’Enter value of c: ’); x = input(’Enter value of x: ’); if a==0 & b==0 & c==0 & x==0
break % Terminates or breaks the loop end
quadratic = a*x^2 + b*x + c; disp(’Quadratic result:’) disp(quadratic)
end

## Slide 12: Programs for Practice:
Problem 1: A can of soda at temperature 25oC is placed in a refrigerator, where the ambient temperature F is 10oC. We want to determine how the temperature of the soda changes over a period of time. A standard way of approaching this type of problem is to subdivide the time interval into a number of small steps, each of duration Δt. If Ti is the temperature at the beginning of step i, the following model can be used to determine Ti+1: Ti+1 = Ti + KΔt(F − Ti); where K is the conduction coefficient, a parameter that depends on the insulating properties of the can and the thermal properties of the soda. Assume that units are chosen so that time is in minutes and that an interval Δt = 1 minute provides sufficient accuracy. Write a Matlab script to compute, display, and plot this update process for K = 0.05.
Solution Tips:
The statement T = zeros(1,101) preallocates a row vector with
101 columns which forms a container for the hundred subsequently recorded temperatures of the soda with a step of 1 minute.
Why use For loop? Because same formula has to be calculated 100 times.
‘disp’ command plots the table of values.
% Define input values
K = 0.05; % Conduction coefficient
F = 10; % Refrigerator temperature (degrees C)
% Define vector variables
t = 0:100; % Time variable (min)
T = zeros(1,101); % Preallocate temperature vector T(1) = 25; % Initial soda temperature (degrees C)
% Update to compute T
for i = 1:100; % Time in minutes
T(i+1) = T(i) + K * (F - T(i)); % Compute T end
% Display results every 10 minutes, plot every minute
fprintf (' %6s %12s\n' ,'Time','Temperature') disp([ t(1:10:101)' T(1:10:101)' ])
plot(t,T),grid,xlabel('Time (min)'),ylabel('Temperature (degrees C)'),title('Cooling curve')
Points to Ponder:
How FOR loop generates the desired result?
How the table of time vs temperature is plotted?

## Slide 13
Problem 2: Figure shows a ship sailing on bearing 315o (NW) with a speed of 20 knots. The local current due to the tide is 2 knots in the direction 67.5o (ENE). The ship also drifts at 0.5 knots under wind in the direction 180◦. Calculate the true ship speed, that is, the ship speed with respect to the ocean bottom. Calculate the true ship course, that is, the direction of sailing w.r.t. ocean bottom, measured in degrees clockwise from north.
A Matlab script is written to accomplish the following tasks:
Represent the ship velocity as a vector S, the flow velocity of local current as a vector C, and the wind-drift velocity as vector W.
Calculate the true-velocity vector T (velocity with respect to the ocean bottom) as the vector sum of three calculated quantities. The vectors are resolved along North (first component) and East (the second component).
Calculate the ship's true course with respect to ocean bottom. Note the three speeds are sought as inputs from the user to make program more flexible and remind you about the importance of using 'input' command.

## Slide 14
%Matlab script for calculating true velocity and direction of a cruising ship
VShip = input ('Enter ship speed (in knots)');
VCurrent =input('Enter speed of current');
VWind= input('Enter wind speed');
disp('Ship velocity vector:')
S = VShip*[cos(315*pi/180) sin(315*pi/180)] % ship vector
disp('Current velocity vector:')
C = VCurrent*[cos(67.5*pi/180) sin(67.5*pi/180)] % current vector
disp('Wind drift velocity vector:')
W = VWind*[-1 0] % wind vector 10.disp('True velocity vector:')
11.T = S + C + W
12.disp('Ship speed (knots):')
13.TrueSpeed = norm(T) % calculated by squaring the 2 terms of vector T, adding
14. % them and then taking square of the sum
15.course = atan2(T(2),T(1))*180/pi; % calculates arctangent from X and Y values: ship course, degrees
16.if course < 0
17.course = 360 + course; % correct course if negative 18.end
disp('Actual Ship course (degrees)')
course

## Slide 15: As a suggestion, while running the program enter 20 as ship speed, 3 for the current velocity and wind speed as 0.5.
The evaluated results after running the program are shown below, the values will differ if you provide the inputs different from the ones given above:
Ship velocity vector:
S =
14.1421 -14.1421
Current velocity vector: C =
1.1481 2.7716
Wind drift velocity vector: W =
-0.5000 0
True velocity vector: T =
14.7902 -11.3705
Ship speed (knots):
TrueSpeed = 18.6558
Actual Ship course (degrees) course = 322.4474

## Slide 16: Week 2 Exercises for CANVAS submission
1. You are given a vector x=[12 64 25]. You offer the user THREE options to plot the data as a bar graph, pie chart or a 3-D pie diagram. The Matlab commands for these plot types are ‘bar’, ‘pie’ and ‘pie3’ respectively. Using switch-case structure, initially take input from the user that which type of plot he or she chooses then plot the selected type of plot. As a hint, the first few lines of your program may be:
x = [12 64 25];
plottype = input('Which type of plot do you like(bar, pie2D or pie3D :','s');
switch plottype case 'bar'
bar(x)
title('Bar Graph')……complete the rest of coding

## Slide 17
2. A well-known formula in Fluid Mechanics is the Continuity Equation. It simply enunciates the basic condition for continuity of fluid flow in a conduit
or pipe. For a liquid whose density does not change during ordinary flow velocities, the continuity equation can be written as follows:
(Flow velocity) x (cross-sectional area of pipe) = constant.
An Engineer has to test the flow velocities in three pipes of size 400, 500 and 600 mm over the following flow ranges (in m3/s): [0.2 0.35 0.4 0.5 0.55 0.6
0.65 0.7]. He actually wants to find out that in which case velocity of flow is exceeding 3.5 m/s; this value is the threshold for flow with acceptable noise due to turbulence and friction. The script printed below is one of many ways to solve the given problem. Students are required to add comments to explain how the program structure consisting of two FOR-loops and one IF- construct is working. Also can you improve the display of results?
1. %This program uses FOR Loop to calculate the values of velocity for a given number of Flow rates and Pipe diameters. IF loop is used to testify for the % velocity values falling outside the acceptable range for "Flow with acceptable noise". The formula used is well-known Continuity Equation.
2.
clear u v; clc;
Flow=[0.2 0.35 0.4 0.5 0.55 0.6 0.65 0.7];%Different flow rates arranged as a vector
PipeDia=[0.4 0.5 0.6]; % More than one pipe diameters TO BE CHECKED
u=length(PipeDia);
v=length(Flow); 8.
for m=1:u % Counter for three pipe sizes
Area(m)= (pi/4)*(PipeDia(m)^2);
for n=1:v % Velocity for 8 flow rates will be calculated for every pipe dia.
Velocity(m,n)= Flow(n)/Area(m);
if Velocity(m,n)>3.5
fprintf('For Flow =%4.4f cu.m/s\n',Flow(n))
fprintf('and Pipe Size =%4.4f m',PipeDia(m))
disp('; Velocity over Acceptable Value')
end
end
% Now the program will go to second pipe size and re-calculate velocity for 8 flow rates again.
end 21.
% prints the Flow rate values on screen
disp(‘For the given flow rates, computed velocity values are:')
fprintf('\nFor Pipe Diameter = %4.4f metres\n',PipeDia(1))
disp('Velocity=');Velocity (1,:)
disp ('For Pipe Diameter = '), disp(PipeDia(2))
disp('Velocity ='); Velocity (2,:)
disp ('For Pipe Diameter = '), disp(PipeDia(3))
disp('Velocity ='); Velocity (3,:)